## Slide 1: Diode Types
Solar Cell
Photo Diode
Light Emitting Diode
Schottky Barrier Diode
Zener Diode

## Slide 2: Light Emitting Diodes (LED)
A PN junction diode, which emits light when forward biased, is known as light emitting diode.
The emitted light may be visible or invisible
The amount of light output is directly proportional to the forward current.
Thus higher the forward current, higher is the light output

## Slide 3: Light Emitting Diodes (LED)
The schematic symbol of a light emitting diode is shown in figure.
The arrows pointing away from the diode symbol represent the light, which is being transmitted away from the junction.
Cathode K
Anode A
Circuit symbol

## Slide 4: Light Emitting Diodes (LED)
Cathode K
Anode A
Circuit symbol
sign: | + | -
terminal: | anode (A) | cathode (K)
leads: | long | short
exterior: | round | flat
interior: | small | large
wiring: | red | black
*marking: | none | stripe
*pin: | 1 | 2
*Die placement: | connector | cup
Electrical polarity

## Slide 5: FIGURE 3-30 Typical LEDs.
Thomas L. Floyd Electronic Devices, 6e and Electronic Devices: Electron Flow Version, 4e

## Slide 6: Construction of LED
The construction of LED is same as that of a p-n junction semiconductor diode.
One of the popular methods of construction of LED is to deposite three semiconductor layers on the substrate as shown in figure.
The active region is exist between the p and n regions. The light emerges from the active side in all the directions when electron hole pairs recombine.
substrate
N-region
Active region
P-region
P – region
Active region
N – region
Substrate
+
-

## Slide 7: Construction of LED
In this particular structure, the LED emit light all the way around the layered structure. Thus the basic layered structure is placed in a tiny reflective cup so that the light from the active layer will be reflected towards desired exit direction.

## Slide 8: Materials and colours
The LEDs use mixtures of Gallium (Ga), Arsenic (As) and Phosphorous (P).
The colour of emitted light is decided by its wavelength which depends on forbidden energy gap.
This gap is different for different mixtures. Hence different mixtures give the different colours.
No. | Mixture used | Symbol | Colour
1 | Gallium Arsenide | GaAs | Infrared, invisible
2 | Gallium Phosphide | GaP | Red or Green
3 | Gallium arsenide Phosphide | GaAsP | Red or Yellow
Silicon and germanium are not used for LEDs because their forbidden gap do not allows the light emission in visible spectrum.

## Slide 9: Principle of LED operation
When the LED is forward biased, the electrons in the n-region will cross the junction and recombine with the holes in the p-type materials.
These free electrons resides in the conduction band and hence at a higher energy level than the holes in the valence band.
When recombination takes place, these electrons return back to the valence band which is at lower energy level than the conduction band.
While returning back, the recombining electrons gives away the excess energy in the form of light. This process is called as electroluminescence.
Conduction band
Valence band
Light output
Forbidden
gap
Recombination of
Holes and electrons

## Slide 10: Principle of LED operation
Conduction band
Valence band
Light output
Forbidden
gap
Recombination of
Holes and electrons

## Slide 11: LED biasing
The voltage drop across a conducting LED is in the range of 1.2 V to 3.2 V, depending on the material used.
This voltage is much higher than that across a conventional diode. The current range of the LEDs available in the market is 10 to 80 mA.
LEDs have extremely low reverse breakdown voltage of the order of 3 to 10 V. So they should not be subjected to high reverse voltage.

## Slide 12: LED biasing
IF
R
Forward biasing
V
IF in mA
Light
output

## Slide 13: Spectral response curves of LED
The graph of output light ( Y light ) versus the wavelength is called as the spectral response curve of an LED.

## Slide 14: Radiation pattern of LED
The radiation pattern is a graph of light output plotted against angle as shown in figure. It gives idea about how directional the given light source is.
The LED is a highly directional source because it radiates only in a particular direction.
Most of the radiated energy is confined within 200 of direction of maximum light.

## Slide 15: Radiation pattern of LED
The radiation pattern is a graph of light output plotted against angle as shown in figure. It gives idea about how directional the given light source is.
The LED is a highly directional source because it radiates only in a particular direction.
Most of the radiated energy is confined within 200 of direction of maximum light.

## Slide 16: Advantages of LEDs
LEDs are of small size and light weight. Therefore it is possible to pack a large number of LED in a small space while manufacturing a display.

## Slide 17: Advantages of LEDs
LEDs are of small size and light weight. Therefore it is possible to pack a large number of LED in a small space while manufacturing a display.
They are available in a different spectral colours.

## Slide 18: Advantages of LEDs
LEDs are of small size and light weight. Therefore it is possible to pack a large number of LED in a small space while manufacturing a display.
They are available in a different spectral colours.
They have larger life as compared to the lamps.

## Slide 19: Advantages of LEDs
LEDs are of small size and light weight. Therefore it is possible to pack a large number of LED in a small space while manufacturing a display.
They are available in a different spectral colours.
They have larger life as compared to the lamps.
The light emitted by a LED is proportional to the amount of current flowing through it. Hence we can control the current flowing through the LEDs to vary their brightness as per the requirements of the application.

## Slide 20: Advantages of LEDs
LEDs are of small size and light weight. Therefore it is possible to pack a large number of LED in a small space while manufacturing a display.
They are available in a different spectral colours.
They have larger life as compared to the lamps.
The light emitted by a LED is proportional to the amount of current flowing through it. Hence we can control the current flowing through the LEDs to vary their brightness as per the requirements of the application.
They are suitable at high operating speeds as they takes less than 1 μs to turn on or off.

## Slide 21: Advantages of LEDs
LEDs are of small size and light weight. Therefore it is possible to pack a large number of LED in a small space while manufacturing a display.
They are available in a different spectral colours.
They have larger life as compared to the lamps.
The light emitted by a LED is proportional to the amount of current flowing through it. Hence we can control the current flowing through the LEDs to vary their brightness as per the requirements of the application.
They are suitable at high operating speeds as they takes less than 1 μs to turn on or off.
LEDs can be easily interfaced with the other electronic circuits

## Slide 22: Disadvantages of LEDs
Output power is affected by changes in temperature.
Over current can damage it easily.
They need larger power for their operation

## Slide 23: Applications of LEDs
In the optocouplers.
In the infrared remote controls.
As indicators in various electronic circuits.
In seven segment and alphanumeric display.

## Slide 24: Comparison of LED and p-n junction diode

## Slide 25: Comparison of LED and p-n junction diode
LED
It emits light, when forward bias.
P-n junction diode

## Slide 26: Comparison of LED and p-n junction diode
LED
It emits light, when forward bias.
P-n junction diode
It does not emits light

## Slide 27: Comparison of LED and p-n junction diode
LED
It emits light, when forward bias.
p-n junction diode
It does not emits light

## Slide 28: Comparison of LED and p-n junction diode
LED
It emits light, when forward bias.
It uses material like gallium arsenide Phosphide and gallium Phosphide.
p-n junction diode
It does not emits light

## Slide 29: Comparison of LED and p-n junction diode
LED
It emits light, when forward bias.
It uses material like gallium arsenide Phosphide and gallium Phosphide.
p-n junction diode
It does not emits light
It uses material like silicon and germanium

## Slide 30: Comparison of LED and p-n junction diode
LED
It emits light, when forward bias.
It uses material like gallium arsenide Phosphide and gallium Phosphide.
The drop across forward biased LED is about 2 V
p-n junction diode
It does not emits light
It uses material like silicon and germanium

## Slide 31: Comparison of LED and p-n junction diode
LED
It emits light, when forward bias.
It uses material like gallium arsenide Phosphide and gallium Phosphide.
The drop across forward biased LED is about 2 V
p-n junction diode
It does not emits light
It uses material like silicon and germanium
The drop across forward biased diode is about 0.7 V.

## Slide 32: Comparison of LED and p-n junction diode
LED
It emits light, when forward bias.
It uses material like gallium arsenide Phosphide and gallium Phosphide.
The drop across forward biased LED is about 2 V
Reverse breakdown voltage is low, about 3 V to 10 V.
p-n junction diode
It does not emits light
It uses material like silicon and germanium
The drop across forward biased diode is about 0.7 V.

## Slide 33: Comparison of LED and p-n junction diode
LED
It emits light, when forward bias.
It uses material like gallium arsenide Phosphide and gallium Phosphide.
The drop across forward biased LED is about 2 V
Reverse breakdown voltage is low, about 3 V to 10 V.
p-n junction diode
It does not emits light
It uses material like silicon and germanium
The drop across forward biased diode is about 0.7 V.
Reverse breakdown voltage is high, about 50 V and more.

## Slide 34: Comparison of LED and p-n junction diode
LED
It emits light, when forward bias.
It uses material like gallium arsenide Phosphide and gallium Phosphide.
The drop across forward biased LED is about 2 V
Reverse breakdown voltage is low, about 3 V to 10 V.
The applications are optocouplers seven segment displays, etc.
p-n junction diode
It does not emits light
It uses material like silicon and germanium
The drop across forward biased diode is about 0.7 V.
Reverse breakdown voltage is high, about 50 V and more.

## Slide 35: Comparison of LED and p-n junction diode
LED
It emits light, when forward bias.
It uses material like gallium arsenide Phosphide and gallium Phosphide.
The drop across forward biased LED is about 2 V
Reverse breakdown voltage is low, about 3 V to 10 V.
The applications are optocouplers seven segment displays, etc.
p-n junction diode
It does not emits light
It uses material like silicon and germanium
The drop across forward biased diode is about 0.7 V.
Reverse breakdown voltage is high, about 50 V and more.
The applications are rectifiers, clippers, clampers, voltage multipliers, etc..

## Slide 36: LEDs configurations
LED displays are packages of many LEDs arranged in a pattern, the most familiar pattern being the 7-segment displays for showing numbers (digits 0-9). The pictures below illustrate some of the popular designs:
Bargraph | 7-segment | Starburst | Dot matrix

## Slide 37: Single Digit Seven-Segment LED Display
Features • Low Current Consumption • High Brightness • Easy to Use • PCB Mounting

## Slide 38: FIGURE The 7-segment LED display.
Thomas L. Floyd Electronic Devices, 6e and Electronic Devices: Electron Flow Version, 4e

## Slide 39: 16-Segment LED Display
Features • Low Current Consumption • High Brightness • Easy to Use • PCB Mounting
Starburst

## Slide 40: 16-Segment LED Display
A sixteen-segment display, sometimes called a "Union Jack" display or a "British Flag" display, is a type of display based on 16 segments that can be turned on or off according to the graphic pattern to be produced. It is an extension of the more common seven-segment display, adding four diagonal and two vertical segments and splitting the three horizontal segments in half (A fourteen-segment display splits only the middle one).
Starburst

## Slide 41: 16-Segment LED Display
Before the advent of inexpensive dot-matrix displays, sixteen and fourteen-segment displays were some of the few options available for producing alphanumeric characters on calculators and other embedded systems. However, they are still sometimes used on VCRs, car stereos, microwave ovens, telephone Caller ID displays, and slot machine readouts.
Starburst

## Slide 42: Dot matrix
A dot matrix is a 2-dimensional array of dots used to generate characters, symbols and images.
The display consist of a matrix of LEDs arranged in a rectangular configuration.
By switching on or off the selected LED’s text or graphics can be displayed.
A matrix driver or controller converts the instructions from a processor into signal which turns on or off LED’s in the matrix
 |  |  | Dot matrix

## Slide 43: Dot matrix
 |  |  | Dot matrix

## Slide 44: 10 LED Bargraph Displays
Features • Low Current Consumption • High Brightness • Easy to Use • PCB Mounting
Bargraph

## Slide 45: Solar Cell
Q: Explain the working of solar
cell with application?
Solar cell: Solar cell is a photovoltaic device that converts the light energy into electrical energy based on the principles of photovoltaic effect

## Slide 46
CLASSIFICATION OF TRANSDUCERS According to Transduction Principle
PHOTOVOLTAIC TRANSDUCTION :
In photovoltaic transduction the measurand is converted to voltage generated when the junction between dissimilar material is illuminated as shown in fig.

## Slide 47
n-type semiconductor
p-type semiconductor
+ + + + + + + + + + + + + + +
- - - - - - - - - - - - - - - - - -
Physics of Photovoltaic Generation
Depletion Zone

## Slide 48
Photovoltaic effect
Definition:
The generation of voltage across the PN junction in a semiconductor due to the absorption of light radiation is called photovoltaic effect. The Devices based on this effect is called photovoltaic device.
Light energy
n-type semiconductor
p- type semiconductor
Electrical Power
p-n junction

## Slide 49
Solar panel (or) solar array (or) Solar module
The solar panel (or) solar array is the interconnection of number of solar module to get efficient power.
A solar module consists of number of interconnected solar cells.
These interconnected cells embedded between two glass plate to protect from the bad whether.
Since absorption area of module is high, more energy can be produced.

## Slide 51: Materials for Solar Cell
Solar cells are composed of various semiconducting materials
  Crystalline silicon
  Cadmium telluride
  Copper indium diselenide
  Gallium arsenide
  Indium phosphide
  Zinc sulphide
Note: Semiconductors are materials, which become electrically conductive when supplied with light or heat, but which operate as insulators at low temperatures

## Slide 52: Construction of Solar Cell
Solar cell (crystalline Silicon) consists of a n-type semiconductor (emitter) layer and p-type semiconductor layer (base). The two layers are sandwiched and hence there is
formation of p-n junction.
The surface is coated with anti-refection coating to avoid the loss
of incident light energy due to reflection.
A proper metal contacts are made on the n-type and p- type side
of the semiconductor for electrical connection

## Slide 53: Working of solar cell
When a solar panel exposed to sunlight , the light energies
are absorbed by a semiconductor materials.
Due to this absorbed energy, the electrons are liberated and produce the external DC current.
The DC current is converted into 240-volt AC current using an inverter for different applications.

## Slide 54: Working of solar cell
It is a pn junction device with no voltage directly applied across the junction.
When light hits the space charge region, electrons and holes are generated.
They are then quickly seperated and swept out of the
space charge region by the electric field, thus creating
PHOTON CURRENT.

## Slide 55: Application
    Soar pumps are used for water supply.
    Domestic power supply for appliances include refrigeration, washing machine, television and lighting
    Ocean navigation aids: Number of lighthouses and most buoys are powered by solar cells
    Telecommunication systems: radio transceivers on mountain tops, or telephone boxes in the country can often be solar powered
    Electric power generation in space: To providing electrical power to satellites in an orbit around the Earth

## Slide 56
Photodiode (pn junction) operated in reverse bias.
Photodiodes
In a reverse biased p-n junction a Reverse Saturation Current flows due to minority carriers which are thermally generated.
Increasing the reverse bias does not increases the reverse current significantly.
TEMPERATURE and ILLUMINATION increases number of minority carriers (reverse) current.

## Slide 57
The photons impacting the junction cause covalent bonds to break.
The electric field in the depletion layer sweeps Minority electrons in p side to n side and minority holes in n side to the p-side.
Reverse current across junction- photocurrent is proportional to the intensity of the incident light.
Response time is fast (nanoseconds)

## Slide 58
Materials used to produce photodiodes
Silicon
Germanium
Indium Gallium Arsenide
Lead Sulphide

## Slide 60
Photodiode Circuit
If photon intensity is zero.
  Only current flowing is the reverse saturation current.
  ( Dark current , normally small ).
Photon intensity of sufficient energy strikes the diode.
  Photoelectric effect ( electron hole pair in
  space charge region)
  Photocurrent flows in reverse direction.
  Photocurrent is sum of dark current and the light current.
  Photocurrent creates voltage drop across R.

## Slide 61: Schottky Diode

## Slide 70: Schottky diode
Advantages:
High speed, high frequency, low forward voltage
drop, low heat dissipation, low loss.
Disadvantages:
Size and cost.